## Slide 1: Introduction
Thread-Level parallelism
  Have multiple program counters
  Uses MIMD model
  Targeted for tightly-coupled shared-memory multiprocessors
For n processors, need n threads
Amount of computation assigned to each thread = grain size
  Threads can be used for data-level parallelism, but the overheads may outweigh the benefit
Slides adapted from Comp. Arch A Quantitative Approach Hennessy and Patterson

## Slide 2: Architectures
Symmetric multiprocessors (SMP)
  Small number of cores
  Share single memory with uniform memory latency
  Uses Snoopy Cache Protocols
Distributed shared memory (DSM)
  Memory distributed among processors
  Non-uniform memory access/latency (NUMA)
  Processors connected via direct (switched) and non-direct (multi-hop) interconnection networks
  Uses Directory Cache Protocol
Slides adapted from Comp. Arch A Quantitative Approach Hennessy and Patterson

## Slide 3: Cache Coherence
Coherence
  All reads by any processor must return the most recently written value
  Writes to the same location by any two processors are seen in the same order by all processors
Consistency
  When a written value will be returned by a read
  If a processor writes location A followed by location B, any processor that sees the new value of B must also see the new value of A
Slides adapted from Comp. Arch A Quantitative Approach Hennessy and Patterson

## Slide 4: Enforcing Coherence
Coherent caches provide:
  Migration: movement of data
  Replication: multiple copies of data
Cache coherence protocols
  Directory based
    Sharing status of each block kept in one location
  Snooping
    Each core tracks sharing status of each block
Slides adapted from Comp. Arch A Quantitative Approach Hennessy and Patterson

## Slide 5: Snoopy Cache Protocols
Write invalidate
  On write, invalidate all other copies
  Use bus itself to serialize
    Write cannot complete until bus access is obtained
Write update
  On write, update all copies
Slides adapted from Comp. Arch A Quantitative Approach Hennessy and Patterson

## Slide 6: Snoopy Coherence Protocols
Locating an item when a read miss occurs
  In write-back cache, the updated value must be sent to the requesting processor
Cache lines marked as shared or exclusive/modified <- Caution: “modified” takes on different meanings for different protocols
  Only writes to shared lines need an invalidate broadcast
    After this, the line is marked as exclusive
Common Snoopy Protocols
MSI: Modified, Shared, Invalid
MESI: Modified, +(Exclusive), Shared, Invalid
MOESI: Mod, +(Owned), Exc. Shared, Invalid
Slides adapted from Comp. Arch A Quantitative Approach Hennessy and Patterson

## Slide 7: Coherence Protocols
Every multicore with >8 processors uses an interconnect other than bus
  Makes it difficult to serialize events
  Write and upgrade misses are not atomic
  How can the processor know when all invalidates are complete?
  How can we resolve races when two processors write at the same time?
  Solution: associate each block with a single bus
Slides adapted from Comp. Arch A Quantitative Approach Hennessy and Patterson

## Slide 8: Directory Based Protocols
Snooping schemes require communication among all caches on every cache miss
  Limits scalability
  Another approach: Use centralized directory to keep track of every block
    Which caches have each block
    Dirty status of each block
Implement in shared L3 cache
  Keep bit vector of size = # cores for each block in L3
  Not scalable beyond shared L3
Slides adapted from Comp. Arch A Quantitative Approach Hennessy and Patterson