## Slide 1: Processor-In-Memory (PIM) Architectures
Domain Specific Architectures
Guest Lecturer
MD Arafat Kabir
Summer Graduate, PhD
Advisor: Dr. David Andrews
Dissertation: Deep-learning FPGA accelerator using PIM architecture

## Slide 2: Earliest Publications
IEEE Transactions on Computers, 1969
Computer, 1995

## Slide 3: What is Processor-in-Memory (PIM)
Main idea: Put memory and processor together (same chip)
CPU
Regfile
ALU
RAM
SRAM
SRAM
SRAM
SRAM
Address
Data
Classic von Neumann Architecture
PIM
SRAM
ALU
SRAM
ALU
SRAM
ALU
SRAM
ALU
PIM Architecture

## Slide 4: SRAM Array
Image source: Google search

## Slide 5: A Practical PIM Design: Cache-based
C. Eckert, X. Wang, J. Wang, A. Subramaniyan, R. Iyer, D. Sylvester, D. Blaauw, and R. Das, “Neural Cache: Bit-Serial in-Cache Acceleration of Deep Neural Networks,” in 2018 ACM/IEEE 45Th annual international symposium on computer architecture (ISCA), 2018, pp. 383–396.

## Slide 6: Why Do We Need PIM Architectures?
What happens in the CPU when you add two vectors?
  C = A+B; A,B,C are vectors of 1000 elements
result[i] = array1[i] + array2[i];
  read array1[i] to register R1
  read array2[i] to register R2
  add R1, R2 and save to R3
  Write R3 to result[i]
for (int i = 0; i < size; i++)
  increment i (R4)
  read size to register R5
  compare R4, R5
  make a conditional jump
void add_vector(int array1[], int array2[], int result[], int size)
{
for (int i = 0; i < size; i++) {
result[i] = array1[i] + array2[i];
}
}
Most of the instructions (90%) are spent on control sequence!

## Slide 7: Why Do We Need PIM Architectures?
“The Memory Wall”
  Memory operations (read/write) are significantly slower than CPU operations.
Cycle latency from Wikipedia
  Corei9: 0.16 ns
  DDR5: 14 ns

## Slide 8: Why Do We Need PIM Architectures?
Memory access cost
  100x slower
  100x more energy
Narrow bus connection
  Limited bus frequency
  Limited number of pins
  One word at a time
Application requirements
  Different access patterns
Domain-specific PIMs,
Smaller arrays can be faster
PIM can minimize energy cost
Not limited by bus frequency or pin count
Match application access pattern
Massive parallelism

## Slide 9: Key Takeaway
PIM architectures can help with
memory-intensive applications.