## Slide 1: Domain Specific Architectures CSCE 4013/5013
David Andrews
Rm 527 JBHT
dandrews@uark.edu
CSCE University of Arkansas
Office Hrs: 3:00 – 4:00 MWF
Class website: https://hthreads.github.io/classes/#eecs-5013-domain-specific-accelerators
Welcome !

## Slide 2: Course Overview
What is a Domain Specific Architecture ?
What we study during the course
What will be your involvement
How you will be graded

## Slide 3: What is a Domain Specific Architecture ?
A Hardware Architecture: Designed for a Specific Domain of Applications. Examples:
  Graphics
  Image Processing
  Deep Learning
General Purpose Architectures: Designed to be flexible enough to do everything but not optimal for anything 
  What was first GP uProcessor ?
  Turing Complete ?

## Slide 4: What is a Domain Specific Architecture ?
Generally Accompanied by a Domain Specific Language:
Python, OpenCL
Pytorch, Tensorflow
Allows expression of the common types of parallelism within the domain
-AI domain dominated by Large Matrix Operations:
i.e., (SIMD) Data level Parallelism
DSL’s are good at what they are targeting but are
not general purpose

## Slide 5: What is a Domain Specific Architecture ?
Domain Specific Accelerators exploit four main techniques to get performance and efficiency:
Data Specialization: Specialized ops on domain specific data types. Can do in one cycle what may take tens of cycles on GP computer.
Exploit Parallelism: Match what is available in the application:
  Locality of reference is key
  global memory references severely degrade performance

## Slide 6: What is a Domain Specific Architecture ?
3. Local and Optimized Memory: Store highly used data structures in small high bandwidth memories close to processing units.
Increase Energy Efficiency
Decrease Processing Latency
4. Reduced Overhead: Specialized hardware and Languages decrease overhead of program interpretation and reduces #instructions.
GP Proc expends ~90% of energy on overhead:
<IF, ID, Data Supply, control>

## Slide 7: How Important is Memory Design?
Area and Power of most accelerators dominated by Memory
-Performance often memory limited

## Slide 8: Accelerator Costs
Op | Energy | Area
8-bit Add | 10 fJ | 4 um 2
Small (8 Kbyte) SRAM Local | 50 fJ/bit | .013 um 2 per bit
Larger (100 MB) SRAM Local | .7 pJ/bit | 
Global memory | 4 pJ/bit | 
Local Comm (on Chip) | 100fJ/bit-mm | Linear Increase
Global Comm (off Chip) | 10 pJ/bit | 

## Slide 9: The Big Three:
Graphics Processing Units (GPUs)
  NVIDIA ~88%. (~98% of data center market)
  AMD ~12%
  Intel ~0%
Field Programmable Gate Arrays (FPGAs)
  Xilinx -> AMD
  Altera -> Intel -> Altera (split being completed)
Application-Specific Integrated Circuits (ASICs)
  Google: Tensor Processing Unit (TPU)
  Microsoft: Athena this year
  Amazon Web Services:
  Some Interesting Startups: Cerebras, Groq

## Slide 10: What will we study ?
Review of key concepts and technology trends
Array Processors/Systolic Arrays
Processor near/in Memory architectures
Case Studies
Crystal Ball gazing:

## Slide 11: What is Your Responsibility?
Advanced Senior Level/Graduate Class: Topics and technologies continue to develop. Materials are from Conferences/Journals and not textbooks.
-Attend Class!
-Read papers before we discuss in class
-Attend class!
-Come prepared to engage in discussions
-Attend Class!

## Slide 12: How will you be graded ?
Presentations: 30%
Quizzes: 30%
Participation: 10%
Final Project: 30%