## Slide 1
Slides are Adapted from
Parallel Computer Architecture and Programming CMU 15-418/15-618, Spring 2019
Directory Based Cache Coherence
CSCE 4213 Introduction to Computer Architecture
David Andrews

## Slide 2: Implementing cache coherence
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Interconnect
Memory
I/O
The snoopy cache coherence protocol relies on
Single bus to broadcast coherence information to all processors
All caches monitoring all bus traffic “snoop” and take appropriate action
“Broadcast doesn’t scale past a handful of processors

## Slide 3: Scaling cache coherence to large machines
Processor
Local Cache
Memory
Processor
Local Cache
Memory
Processor
Local Cache
Memory
Processor
Local Cache
Memory
Interconnect
Recall non-uniform memory access (NUMA) shared memory systems
Idea: locating regions of memory near the processors increases scalability: it yields higher aggregate bandwidth and reduced latency (especially when there is locality in the application)
But... efficiency of NUMA system does little good if the coherence protocol can’t also
be scaled!
Consider this case: processor accesses nearby memory (good...), but to ensure coherence still must broadcast to all other processors it is doing so (bad...)
Some terminology:
cc-NUMA = “cache-coherent, non-uniform memory access”
Distributed shared memory system (DSM): cache coherent, shared address space, but architecture implemented by physically distributed memories

## Slide 4: Scaling cache coherence in current multicores
Mem Ctrl
Mem Ctrl
Mem Ctrl
Mem Ctrl
ccNUMA typically refers to supercomputing/clusters
Same issues appear in multicores
  NUMA: Memory controllers distributed around chip
  NUCA (non-uniform cache access): L3 banks distributed around the chip too
Core L3 Cache Bank

## Slide 5: Scalable cache coherence using directories
Snooping schemes broadcast coherence messages to determine the state of a line in the other caches
Alternative idea: avoid broadcast by storing information about the status of the line in one place: a “directory”
  The directory entry for a cache line contains information about the state of the cache line in all caches.
  Caches look up information from the directory as necessary
  Cache coherence is maintained by point-to-point messages between the caches on a “need to know” basis (not by broadcast mechanisms)

## Slide 6: A very simple directory
Scalable Interconnect
Processor
Local Cache
Directory
Memory
. . .
One line of memory
One directory entry per line of
memory
P presence bits: indicate whether processor P has line in its cache
Dirty bit: indicates line is dirty in one of the processors’ caches
Line: A region of memory that would be cached as a single block (e.g., 64 bytes)

## Slide 7: So we’ve traded a bus bottleneck for a memory bottleneck?
Not quite; directories distributed across memory banks
  Different ordering points for different addresses
Can cache directory entries + avoid memory access
  Caches are much faster + higher bandwidth than memory

## Slide 8: A distributed directory in ccNUMA
Scalable Interconnect
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
“Home node” of a line: node with memory holding the
corresponding data for the line
Example: node 0 is the home node of the yellow line, node 1 is the home node of the blue line
“Requesting node”: node containing processor requesting line
Example: directory partition is co-located with memory it describes

## Slide 9: A distributed directory in a multicore
As we shall see, directories really live in each L3 bank
Core L3 Cache Bank
Mem CDtirl
Mem CDtirl
CDtirl
Dir
Dir Dir Dir Mem
CDtirl
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir Mem
Dir
Dir
Dir
Dir

## Slide 10: Example 1: read miss to clean line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is not dirty
1. Request: read miss msg
Read miss message sent to home node of the requested line
Home directory checks entry for line
Scalable Interconnect

## Slide 11: Example 1: read miss to clean line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is not dirty
Request: read miss msg
Response (line of data from memory)
Read miss message sent to home node of the requested line
Home directory checks entry for line
- If dirty bit for cache line is OFF, respond with contents from memory, set presence[0] to true
Scalable Interconnect
(to indicate line is cached by processor 0)

## Slide 12: Example 2: read miss to dirty line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contents in P2’s
cache)
Request: read miss msg
Response: owner id
If dirty bit is ON, then data must be sourced by another processor (with the most up-to- date copy of the line)
Home node must tell requesting node where to find data
- Responds with message providing identity of line owner (“get it from P2”)
Scalable Interconnect

## Slide 13: Example 2: read miss to dirty line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contents in P2’s
cache)
Request: read miss msg
Response: owner id
Request: data
Response: data
If dirty bit is ON, then data must be sourced by another processor
Home node responds with message providing identity of line owner
Requesting node requests data from owner
Owner changes state in cache to SHARED (read only), responds to requesting node
Scalable Interconnect

## Slide 14: Example 2: read miss to dirty line
Spring 2019
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contents in P2’s
cache)
memory
1. Request: read miss msg
Response: owner id
Request: data
If dirty bit is ON, then data must be sourced by another process4o. rResponse: data
Home node responds with message providing identity of line owner
Requesting node requests data from owner
Owner responds to requesting node, changes state in cache to SHARED (read only)
Owner also responds to home node, home clears dirty, updates presence bits, updatesCMU 15-418/618,
5. Response: data+dir revision
Scalable Interconnect

## Slide 15: Example 3: write miss
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
1. Request: write miss msg
Scalable Interconnect

## Slide 16: Example 3: write miss
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
Request: write miss msg
Response: sharer ids + data
Scalable Interconnect

## Slide 17: Example 3: write miss
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
Request: write miss msg
Response: sharer ids + data
Request: invalidate (2 msgs)
Scalable Interconnect

## Slide 18: Example 3: write miss
Scalable Interconnect
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
Request: write miss msg
Response: sharer ids + data
Request: invalidate (2 msgs)
4b. Response: ack from P1
4a. Response: ack from P2
After receiving both invalidation acks, P0 can perform write

## Slide 19: Advantage of directories
On reads, directory tells requesting node exactly where to get the line from
  Either from home node (if the line is clean)
  Or from the owning node (if the line is dirty)
  Either way, retrieving data involves only point-to-point
communication
On writes, the advantage of directories depends on the number of sharers
  In the limit, if all caches are sharing data, all caches must be communicated with (just like broadcast in a snooping protocol)

## Slide 20: Cache invalidation patterns
64 processor system
Ocean
Barnes-Hut
Number of sharers 
LU
0 1 2 3 4 5 6 7
8 to 11
12 to 15
16 to 19
20 to 23
24 to 27
28 to 31
32 to 35
36 to 39
40 to 43
44 to 47
48 to 51
52 to 55
56 to 59
60 to 63
Graphs plot histogram of number of sharers of a line at the time of a write
In general only a few processors share the line (only a few processors must be told of writes)
Not shown here, but the expected number of sharers typically increases slowly with P (good!)

## Slide 21: In general, only a few sharers during a write
Access patterns
  “Mostly-read” objects: lots of sharers but writes are infrequent, so
minimal impact on performance (e.g., root node in Barnes-Hut)
  Migratory objects (one processor reads/writes for while, then another, etc.): very few sharers, count does not scale with number of processors
  Frequently read/written objects: frequent invalidations, but sharer count is low because count cannot build up in short time between invalidations (e.g, shared task queue)
  Low-contention locks: infrequent invalidations, no performance problem
  High-contention locks: can be a challenge, because many readers present when lock released
Implication 1: directories are useful for limiting coherence traffic
  Don’t need a broadcast mechanism to “tell everyone”
Implication 2: lets us limit directory storage overhead (how?)

## Slide 22: Optimizing directory-based coherence
Reducing storage overhead of directory data structure
  Limited pointer schemes
  Sparse directories
Reducing number of messages sent to implement coherence protocol

## Slide 23: Recall: read miss to dirty line
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s
cache)
1. Request: read miss msg
Scalable Interconnect

## Slide 24: Recall: read miss to dirty line
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s
cache)
(Note: figure below shows final state of system after operation is complete)
1. Request: read miss msg
Response: owner id
Request: data
Response: data
Five network transactions in total
Four of the transactions are on the “critical path” (transactions 4 and 5 can be done in parallel)
- Critical path: sequence of dependent operations that must occur to complete operation
5. Response: data+dir revision
Scalable Interconnect

## Slide 25: Intervention forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s
cache)
1. Request: read miss msg
Scalable Interconnect

## Slide 26: Intervention forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s
cache)
1. Request: read miss msg
3. Response: data+dir revision
2. Request: intervention read
Home node requests data from owner node (processor 2)
Owning node responds
Scalable Interconnect

## Slide 27: Intervention forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s
cache)
1. Request: read miss msg
3. Response: data+dir revision
2. Request: intervention read
4. Response: data
4. Home node updates directory, and responds to requesting node with data
Four network transactions in total (less traffic)
But all four of the transactions are on the “critical path.”
Can we do better?
Scalable Interconnect

## Slide 28: Request forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s
cache)
1. Request: read miss msg
Scalable Interconnect

## Slide 29: Request forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s
cache)
1. Request: read miss msg
2. Request: send data to requestor
Scalable Interconnect

## Slide 30: Request forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s
cache)
1. Request: read miss msg
2. Request: send data to requestor
3/4. Response: data
(2 msgs: sent to both home node and requestor)
Four network transactions in total
Only three of the transactions are on the critical path (transactions 3 and 4 can be done in parallel) Note: system is no longer pure request/response (since P0 sent request to P1, but receives response
from P2)
Scalable Interconnect

## Slide 31: Directory coherence in Intel Core i7 CPU
L3 hosts in-cache directory (and is inclusive)
Directory maintains list of L2 caches containing line
Instead of broadcasting coherence traffic to all L2’s, only send coherence messages to L2’s that contain the line
(Core i7 interconnect is a ring, it is not a bus)
Directory dimensions:
- P=4
- M = number of L3 cache lines
Core
L1 Data Cache
L2 Cache
 | Shared L3 (One bank | Cache per core) | 
Ring Interconnect
Core
L1 Data Cache
L2 Cache
Core
L1 Data Cache
L2 Cache
Core
L1 Data Cache
L2 Cache

## Slide 32: Coherence in multi-socket Intel systems
Core
L1
L2
 | L3 Cac | he | 
Core
L1
L2
Core
L1
L2
Core
L1
L2
Core
L1
L2
 | L3 Cac | he | 
Core
L1
L2
Core
L1
L2
Core
L1
L2
Cache Agent
Cache Agent
Memory Controller
Memory Controller
Home Agent
Home Agent
QuickPath Interconnect (QPI)
to DRAM…
(with in memory
directory)
Dir cache (16KB)
Dir cache (16KB)
to DRAM…
(in memory directory)
L3 directory reduces on- chip coherence traffic (previous slide)
In-memory directory (cached by home agent/memory controller) reduces coherence traffic between cores

## Slide 33: Xeon Phi
Intel’s NUMA on a chip
Many (50+) x86 cores
  Ours have 61
  “Knight’s Corner”
  4-way hyper threading
  Each with 1–2 vector units
Cache-coherent memory system
Knight’s Corner overall system:
  Max. 8GB memory
  Max. 2 TFLOPS
  0.004 bytes/flop
not balanced
300 Watts
Prototype / internal names include:
Larrabee, Knight’s Ferry, Knight’s Corner, Knight’s Landing, Knight’s Hill
China’s Tianhe-2 has 48,000
Knight’s Corner chips

## Slide 34: Knight’s Corner Xeon Phi Cache Coherence
512KB L2 caches
8 memory controllers
  Total 8GB max.
Prototype / internal names include:
Larrabee, Knight’s Ferry, Knight’s Corner, Knight’s Landing, Knight’s Hill

## Slide 35: KC Xeon Phi Ring Communication
Messages sent around bidirectional ring
  Having everything on single chip enables very wide communication paths
  Can get effect of broadcast by circulating message around entire ring
- Advantage over point-to-point

## Slide 36: KC Xeon Phi Directory Structure
Directory keeps track of which lines are resident in local L2
- Same as with single-node system
Worst-case memory read or write by P:
  Check local cache
  Circulate request around ring for line in some cache
  Send request around ring to memory controller

## Slide 37: Next Generation Xeon Phi
“Knight’s Landing”
72 cores
  Each with 4-way hyper threading
  Each with 2 vector units
Grouped into pairs to give 36 compute nodes
Peak 6 SP TFLOPS
16 GB on package RAM
Access to up to 384 GB off-package RAM

## Slide 38: Knight’s Landing Xeon Phi Cache Coherence
Nodes organized as 2-D mesh
  Some for computation
  Some for memory interfaces
Use X/Y routing to send messages
Must use more traditional directory-based scheme

## Slide 39: Summary: directory-based coherence
Primary observation: broadcast doesn’t scale, but luckily we don’t need to broadcast to ensure coherence because often the number of caches containing a copy of a line is small
Instead of snooping, just store the list of sharers in a
“directory” and check the list as necessary
One challenge: reducing overhead of directory storage
  Use hierarchies of processors or larger line sizes
  Limited pointer schemes: exploit fact the most processors
not sharing line
  Sparse directory schemes: exploit fact that most lines are not in cache
Another challenge: reducing the number of messages sent (traffic) and critical path (latency) of message chains needed to implement coherence operations
Ring-based schemes can be much simpler than point-to-point communication